## Slide 1: Verilog-AMS - Chapter 7: Mixed Signal

## Slide 2: Overview
• Enables analog, digital, and mixed-signal modeling
• Mixed-signal blocks allow analog ↔ digital exchange
• Uses connect modules for interfacing

## Slide 3: Domains
• Continuous (analog): voltages, currents
• Discrete (digital): logic values, registers
• Variables must match their domain context

## Slide 4: Contexts
• Analog context: analog, analog initial
• Digital context: initial, always, assign
• Variables cannot cross contexts directly

## Slide 5: Nets, Nodes, Ports
• Nets: wires/signals
• Nodes: connection points
• Ports: input/output/inout
• Types: Analog, Digital, Mixed

## Slide 6: Behavioral Interactions
• Digital in analog: V(net), I(net)
• Analog in digital: cross(), transition(), idt()
• Enables bridging between domains

## Slide 7: Connect Modules
• Bridge analog and digital ports
• Handle transitions, preserve timing
• Inserted manually or automatically

## Slide 8: Connect Module Syntax
Example:
connectmodule d2a (in, out);
input in;
output out;
ddiscrete in;
electrical out;
...
endmodule

## Slide 9: Example
connectmodule voltage_to_logic(inout electrical vin, logic lout);
parameter real vth = 2.5;
analog begin
lout = (V(vin) > vth) ? 1'b1 : 1'b0;
end
endconnectmodule

## Slide 10: Connect Specification Statements
• connect ... split → one per port
• connect ... merged → group ports
• Example:
connect d2a merged input ttl, output electrical;

## Slide 11: Auto-Insertion of Connect Modules
• Inserted post-elaboration
• Based on port disciplines
• Controlled by connect_mode, supply resolution

## Slide 12: Signal Segmentation
• Digital segmented by connect modules
• Analog nodes remain unified
• Models loading and isolation

## Slide 13: Driver-Receiver Segregation
• Prevents domain conflicts
• Groups receivers and drivers
• Ensures accurate signal flow

## Slide 14: Summary
• Domain bridging via connect modules
• Behavioral interactions across contexts
• Critical for accurate AMS co-simulation